FabOS
a.k.a.: Fabian's OS

Programmers guide

© 2010 Fabian Huslik
# What is FabOS
FabOS is a lightweight embedded operating system aimed for small 8-bit processors and is completely written in C using as less RAM and code space as possible.
It is -as far as possible- independent of the compiler and processor used, therefore it is quite easy to port it to another processor type or compiler.

Footprint:
For 4 Tasks (including idle) with 3 Mutexes it takes 29 to 41 bytes RAM and 1670 to 1932 bytes code. This values are net values. The stack space for every task and possibly used queue space is to be added.

Key features:
- Preemtive real time task scheduling
- Mutexes with priority inversion
- Up to 8 Events per task
- User defined Queues
- Several timed Alarms per Task
- Flexible OS-tick timer interrupt - any interrupt source can be used for scheduling
- The scheduling interrupt remains usable for the application
- Idle task, which runs on "native" stack
- Optional run-time checks
- Easy to use and to understand
# License Agreement
This software is subject to copyright law.
## A short summary of the license agreement:
- Free usage for evaluation, education and private purposes.
- For commercial use a (payed) license is mandatory.
- Entitled to support or warranty only in case of a commercial license.
- No liability by the author
- No copying / transmission / retransmission execept approved by the author.

The fee for a commercial license with support and warranty is cheaper than you might expect, please request without obligation.
## By using the software, you are bound to the following binding agreement:
The software is entrusted to the one it was originally sent, or to whom a download link has been sent.
Any further distribution of this software on any media or public networks is permitted only with prior permission of the author.
The further development or modification of certain files ("FabOS.c and FabOS.h") is only permitted if the author is informed directly. Please use the contact form or mail.

For commercial use a commercial software license is required.
Using the software in home environment, education or evaluation is free of charge.

No liability for certain intended purposes:
The author does not warrant that the software is fit for specific purposes required by the customer, or is compatible to software provided by the customer.
The customer is solely responsible for configuration, testing and use of his system, and for the intended and unintended results.

No liability for consequential damages:
With the exception of gross negligence or willful damage, the author is not liable for damages whatsoever caused by the use of or the inability to use the software.
This applies without exception for lost profits, business interruption, loss of data or other economic loss, even if the author previously advised of the possibility of such damage.

The software is not designed for use in applications where a possible malfunction endangers, directly or indirectly, property or the health, physical integrity or life of a human.
The customer is responsible for validation, testing, qualification and -if necessary- certification of the entire system and has therefore the responsibility for all consequences.

Warranty:
In the case of a commercial license, the warranty period is 12 months from delivery for the functionality of the software in spirit of the description.
Moreover, the legal requirements of the Civil Code (german BGB) are to be followed.
Warranty claims are fulfilled by correcting defective software. Faulty software is not to be used before the correction of the error.
This guaranty does not apply if the malfunction of the software is caused by misuse or incorrect application by customers or third parties.
For a corrected version the author does offer a warranty for the remainder of the original warranty period, but not less than 30 days after delivery of the correction.

Should a clause be here legally invalid, it should be replaced with the help of common sense so that the original meaning can be fulfilled as possible.

We live in Germany ... therefore, a contract with a disclaimer is unfortunately necessary.

# Concepts
This is a static operating system.
The switching of the tasks is done in a non-cooperative way, so called preemptive task switching. The task switch is done by storing the context (all registers + CPU state) on top of the stack of the task and restoring the context of the other task.
After the safe and restore operation, the processing of the task is continued, as if nothing happened.
The interrupt stack resides on top of the stack of the actual task.
There is an idle task, which is executed, if no other task is ready to run.

A System consists of some tasks, which are declared as a “void” function with the following structure:
void myTask(void)
{
while(1)
{
 … your code …
}
}
Each if this task-functions consists of an eternal loop with your instructions.
The switching between the tasks is then done preemptively by the task-switching interrupt.
Each task has its own stack, provided by a globally declared byte array.
The idle task does not have a stack-array declared. Instead it uses the unused "ordinary" stack at the end of RAM. The idle task consists of an infinite loop placed after the call of OS_StartExecution().
Restrictions:
- This is a static operating system.
- A OS element once created, exists forever.
- The use of malloc() is not preferred in a static environment.
- One Task has a fixed priority, which is at the same time the task ID. Lower IDs come first.
- Queues are static.

There are some macros defined to ease the configuration.
Please take a look at the example code for clarification.
# Set up of the operating system
The set-up of the operating system is done at two points.
- the FabOS_config.h file and
- the main entry file of your application.
## User configuration in FabOS_config.h
#define OS_NUMTASKS 3
Set the total number of tasks excluding the idle task. (number of OS_CreateTask – function calls)
The maximum number is 8. This limitation can be changed by the author upon request.

#define OS_NUMMUTEX 3
Set the total number of different mutexes.
The maximum number is limited to 255.

#define OS_NUMALARMS 5
Set the total number of different Alarms.
The maximum number is limited to 255.

#define OS_ScheduleISR TIMER1_COMPA_vect
Preset the interrupt vector which is used for task scheduling.
The user has to set up the cyclic timer interrupt within the CPU_Init() function.
If any additional code has to be executed in this interrupt, the function "OS_CustomISRCode() " can be filled with this code.

#define OS_USECLOCK 1
Enable the use of a 32-bit OS tick counter, which can be read by OS_GetTicks(uint32_t* pTime)

#define OS_USECOMBINED 1
Use "OS_WaitTicks()" and "OS_WaitEventTimeout()" which is easier to use, than combining alarms and events to get the functionality.

#define OS_USEEXTCHECKS 1
Prevent false API usage (e.g. waiting in idle task)

#define OS_USEMEMCHECKS 1
Enable the OS_get_unused_Stack function.

#define OS_UNUSEDMASK 0xee
Set the value to be written into unused memory.
Used by "OS_get_unused_Stack()"

#define OS_TRACE_ON 1
Enable trace to OS_Tracebuffer[]. The number of the OS_TRACE(n) macro is written into the OS_Tracebuffer array, when executing the OS-Code.
The actual(next) buffer is found in the OS_TracebufferIdx variable.
Setting this define to 0 fully disables the tracing and therefore needs no additional resources.

#define OS_TRACESIZE 1000
Size of OS_Tracebuffer[] (in bytes)
## OS_DeclareTask(TaskName, StackSize);
This is a macro for the task function prototype definition, as well as the stack allocation. It is to be used before main(), where the global variables are declared. The task name is then used as the name of the void function, which declares the task. For the stack, the prefix “OSStack” is prepended inside the macro.

Stack size is given in bytes for each task. The space must be dimensioned at least 34 bytes larger than calculated for the program flow, because the task context is stored there at a task change. Provide extra stack space on top for interrupts, because every interrupt can occur within every task.

The remaining unused stack size can be checked by t OS_get_unused_stack(TaskID) function.

An example may look like:
OS_DeclareTask(myTask,200);
and expands as follows:
void MyTask(void); // function prototype
uint8_t OSStackMyTask[200]; // task stack definition
## Scheduling Timer
The used timer interrupt is to be defined in FabOS_config.h for example:
#define OS_ScheduleISR TIMER1_COMPA_vect
Or any other valid interrupt of the processor.

In the CPUinit() the used timer interrupt is to be set up with global interrupts disabled. An useful frequency for the ISR may be 1 to 10 ms, depending on the application.
The user (you) is in charge to make the interrupt happen in the wanted OS cycle time.
If the Interrupt is activated before OS_StartExecution(), the OS will be corrupted.
## void OS_CustomISRCode() ;
This function is to be provided in the users code, if something has to be done in the timer-tick-ISR. This function will be executed inside the ISR context. A good example is to set a compare register to some value to make the next timer interrupt occur at the correct time. The following is only an example.
void OS_CustomISRCode(void)
{
// TODO add your Timer ISR here
TCNT1 =0; // reset the timer on ISR
}
## void CPU_init()
In this function, which is provided by you, initialize the CPU and the timer interrupts including the cyclic task scheduling interrupt, but do not yet enable the global interrupts. This would confuse the scheduler.
## void OS_CreateTask( TaskName, uint8_t taskNum)
Creates a task inside the main function. This function is realized as a macro to simplify the API;
First Parameter is a pointer to a void function, which implements the task. Inside this function all OS – API calls can be used.
Second parameter is the task number, where also the task number defines the tasks priority. Task 0 has the highest priority. Task 7 is the lowest priority. The maximum number of tasks is 8. (so the highest number here is 7)
In a bigger application it may be useful to use macros for the task IDs.

An example may look like:
OS_CreateTask( myTask, 1);
and expands to:
OS_TaskCreateInt(myTask, 1, StackmyTask , sizeof(StackmyTask));
which is the internal task creation function, which joins the task function and the task stack.
## void OS_StartExecution()
Start the operating system; All tasks are executed at least once after start. This function returns, if no task is to be run for the first time. The code after this function call is the idle task. So this function must be followed by an infinite loop. If the following loop exits, there may be an uncontrolled reset of the processor or other strange behaviour.
# The main()
The main() function may look like the following code:

The main function itself:
int main(void)
{
Initialisation of the CPU with global interrupts disabled afterwards:
CPU_init();

The creation of the tasks (up to NUMTASKS) with priority, where 0 is highest prio;
The same priority (also Task ID) must only appear once.:

#define TSKID0 0
#define TSKID1 1
#define TSKID2 2 // in header-file!

OS_CreateTask(Task1, TSKID0);
OS_CreateTask(Task2, TSKID1);
OS_CreateTask(Task3, TSKID2);

The creation of the alarms (up to OS_NUMALARMS) and linking them to Tasks via the Task ID:
One alarm is connected to a task, which it will wake up, if expired.
Several alarm may be connected to the same task.

#define ALMID_A 0
#define ALMID_B 1
#define ALMID_C 2 // in header-file!

OS_CreateAlarm(ALMID_A,TSKID0);
OS_CreateAlarm(ALMID_B,TSKID0); // two alarms are bound to task 0
OS_CreateAlarm(ALMID_C,TSKID1);

Starting of the Operating System:
OS_StartExecution() ;
while(1)
{
// THIS IS the idle task, which must never exit.
}
}

If the main-function exits by accident, the CPU will reset or some other unpredictable results will occur. Do not enable interrupts globally during init. This is done by the call of OS_StartExecution().
# Preemptive tasks
A System also contains some tasks, which are declared as a “void” function with the following structure:
void Task(void) { … your code ...}
A Task must never exit the function. Therefore the following is the minimum for a task.
void Task(void)
{
while(1)
{
// add your code here...
}
// this line must never be hit!
}
If the function exits by accident, the CPU will reset or some other unpredictable results will occur. (e.g. infinite loop with no scheduling active)
The prototype and definition of the task stack via a byte array, is declared by using the macro:
OS_DeclareTask(). (see 4.2 OS_DeclareTask(TaskName, StackSize);)
## Idle task
This is the code, which comes right after OS_StartExecution() in main().
Inside the idle task, it is not allowed to exit the function (so exiting main()) and it is also not allowed to use OS_Wait functions.
Which means, the idle task can only use:
void	OS_SetEvent(uint8_t EventMask, uint8_t TaskID);
void	OS_MutexGet(int8_t mutexID);
void	OS_MutexRelease(int8_t mutexID);
void	OS_SetAlarm(uint8_t AlarmID, uint16_t numTicks );
uint8_t	OS_QueueIn(OS_Queue_t* pQueue , uint8_t byte);
uint8_t	OS_QueueOut(OS_Queue_t* pQueue, uint8_t *pByte);
uint16_t	OS_GetUnusedStack (uint8_t TaskID);
void	OS_GetTicks(uint32_t* pTime);

# Mutexes
## void OS_MutexGet(int8_t mutexNum);
Get a mutex when entering a critical section. If the mutex is occupied, the scheduling will switch to the task, which is blocking the mutex. Otherwise the mutex will be locked and the execution continues right away.
The total number of mutexes is limited to NUMMUTEX.
Trying to get the same mutex twice without releasing it, leads to an eternal loop.
Triggers re-scheduling.
## void OS_MutexRelease(int8_t mutexNum);
Release the mutex at the end of a critical section. A re-scheduling will be done, if another task is waiting for the mutex.
Triggers re-scheduling.
# Alarms
Alarms wake up tasks after a certain time. An Alarm is always assigned to a task.
Alarms have to be pre-configured:

Use the
OS_CreateAlarm(ALARMID, TASKID)
macro to assign an alarm to a task before using it.

## void OS_WaitTicks( uint8_t AlarmID, uint16_t numTicks) ;
Inactivate Task and wait for the specified number of OS ticks.
Triggers re-scheduling. This is a macro, which uses OS_SetAlarm and OS_WaitAlarm internally.
## void OS_SetAlarm(uint8_t AlarmID, uint16_t numTicks );
Set Alarm for own or other task and continue. An alarm timeout will be registered for the specified Alarm. To remove (=cancel) an alarm, set it again with numTicks = 0;
## void OS_WaitAlarm(uint8_t AlarmID, );
Inactivate Task and wait for an alarm to expire.
Triggers re-scheduling.
# Events
OS events are not to be confused with the XMEGA event system, which can of course be used in parallel.
## void OS_SetEvent(uint8_t TaskID, uint8_t EventMask)
Set one or more events (8 bit EventMask) for one task.
Each task has up to 8 events, which are realized by a bitmask.
You can send one or more events to another task. It will wake up, if it waits for at least one of the events. If you send events, and the task is not waiting for it, it will just continue, if it later waits for it. (Events are never lost)
Triggers re-scheduling.
## uint8_t OS_WaitEvent(uint8_t EventMask)
Inactivate Task and wait for one or more events. Return value is the bit-mask of the event(s), which lead to task reactivation. If the return value is zero, the task was activated by an expired alarm. It is unfortunately not possible to see, by which alarm, if more than one alarm is bound to the task.
Triggers re-scheduling.

To do a waitEvent with timeout, you can do:
SetAlarm(MyAlarm, MyTimeout);
ret = WaitEvent(myEventMask);
if (ret == 0) , then you had a timeout.
You have to disable the alarm in case of event success using:
SetAlarm(MyAlarm, 0);
...or just use the following simplified OS_WaitEventTimeout function.

## uint8_t OS_WaitEventTimeout(uint8_t EventMask, uint8_t AlarmID, uint16_t numTicks )
Inactivate Task and wait for an event in combination with a timeout.
Continues, if:
- the timeout has expired (return value is 0)
- if an event had occurred (return value is the event, which lead to activation)
Triggers re-scheduling.

In this function the alarm will be changed. This means, it overwrites a possibly running alarm.
# Queues
The queue memory must be globally declared and initialized as follows:
OS_DeclareQueue(QueueName, NumberOfElements, ElementSize);
It is to be used outside of main(), where global variables are declared.
For example:
OS_DeclareQueue(myQueue,100,4);
declares a Queue named "myQueue" which has room for 100 elements of a size of 4 bytes. Pay attention: the Queue mechanism reserves one element more than declared for empty/full recognition.

Technical information:
The macro
OS_DeclareQueue(myQueue,100,4);
expands to:
uint8_t OSQDmyQueue[101*4]; // OS Queue Data
OS_Queue_t myQueue = {0,0,4,101*4,OSQDmyQueue} // Queue struct

That means, it declares an array for the queue data and a queue struct, which contains the information and pointers to the data array.
## uint8_t OS_QueueIn(OS_Queue_t* pQueue , uint8_t *pByte)
Put an element into a FIFO queue.
Return value is 1 if queue is full, 0 if OK.

A 32bit-value can be stored to a queue as follows, if the queue is declared as above.
ret = OS_QueueIn(&myQueue,(uint8_t*)&my32BitValue);
## uint8_t OS_QueueOut(OS_Queue_t* pQueue, uint8_t *pByte)
Get an element out of a FIFO queue.
Return value is 1 if queue was empty and no data was copied, 0 if OK.
Element size depends on the queue declaration.
The Pointer target must be of the same size as the source.

ret= OS_QueueOut(&myQueue,(uint8_t*)&my32BitValue);
# Internal functions (normally not used by the user)
## ISR (OS_ScheduleISR)__attribute__ ((naked,signal));
Internal, not to be called by the application;
OS tick interrupt function (vector name must be defined in FabOS.h)
## void OS_CreateTaskInt( void (*t)(), uint8_t taskNum, uint8_t *stack, uint8_t stackSize )
Internal, not to be called by the application;
Create a task, function provided as a macro for simplification.
## int8_t OS_GetNextTaskNumber()
Internal: determine the next task to be run according priority.
## void OS_Reschedule()__attribute__ ((naked))
Trigger re-scheduling according the task priorities.
Mostly used internally. Could be used externally, but more or less useless, as most OS-API trigger a reschedule anyway and priority of tasks never changes without using OS-API.
# Helper functions
This functions are available, if the functionality in FabOS_config.h is activated.
## void OS_ErrorHook(uint8_t ErrNo)
For error detection if OS_USEEXTCHECKS == 1 is used, a function of this name has to be provided. An example may look as follows:

void OS_ErrorHook(uint8_t ErrNo)
{
switch(ErrNo)
{
case 2:
// OS_WaitEvent: waiting in idle is not allowed
break;
case 4:
// OS_WaitAlarm: waiting in idle is not allowed
break;
case 5:
// OS_MutexGet: invalid Mutex number
break;
case 6:
// OS_MutexRelease: invalid Mutex number
break;
case 7:
// OS_Alarm misconfiguration
break;
case 8:
// OS_WaitAlarm: Alarm was not active
break;
case 9:
// OS_WaitAlarm: Alarm is not assigned to the task
break;
default:
break;
}
}
The code may be modified as needed.
## uint16_t OS_GetUnusedStack (uint8_t TaskID)
Get the unused stack space in bytes for any task.
The parameter is the Task ID. For the idle task specify NUMTASKS.
## void OS_GetTicks(uint32_t* pTime)
Get the elapsed OS-ticks (count of elapsed OS-ISR events)
Can be used to implement a precise time information.
## uint8_t OS_GetQueueSpace(OS_Queue_t* pQueue)
Get the number of unused queue elements in a queue.
The parameter is a pointer to the queue.
space = OS_GetQueueSpace(&TestQ);
# Programming hints
## Create a cyclic task
To create a cyclic task, just set an alarm for the next activation directly after waiting for it. "myOS.CurrTask" could be replaced by the task ID.
void myCyclicTask()
{
OS_CreateAlarm(OSALMCyclicRepeat, OSTSKCyclic); // maybe in main()

OS_SetAlarm(OSALMCyclicRepeat,10);
while(1)
{
OS_WaitAlarm(OSALMCyclicRepeat);
OS_SetAlarm(OSALMCyclicRepeat,10);

// this is a cyclic task, which runs exactly every 10 ticks

// TODO add your code here
}
}
Attention: do not use the same alarm again within this task.
To have cyclic tasks, which can wait for alarms, use another Alarm bound to this task to provide further delays within this task.

# Program example
This is the main.c of a onboard datalogger.
The Code, which actually does stuff, is omitted here.
The numerical defines for the Alarm IDs start with ALM_
The numerical defines for the Task IDs start with TSK_
The numerical defines for the Mutexes start with Mutex

/*
GPS-Logger

Features:
* RTC Time-Keeping
* GPS serial analysis NMEA
* g-meter analog
* 4 analog inputs
* DS18S20 temperature sensor
* Power good sensing
* SD-card
* LCD

Tasks:

LCD (1s)
DS18S20 acquisition (bit-banging)
AD conversion including g-meter (+int)
SD-card writing with power good from ISR
NMEA GPS-analysis (+int)
Idle: RTC
*/

#include "OS/FabOS.h"
#include "nmea.h"
#include "main.h"

OS_DeclareTask(TaskSD,200);
OS_DeclareTask(TaskDS1820,200);
OS_DeclareTask(TaskADC,200);
OS_DeclareTask(TaskLCD,200);
OS_DeclareTask(TaskNMEA,200);

OS_DeclareQueue(NMEAQueue,50,1); // type: OS_Queue_t

#define MutexIO 0
#define MutexGPS 1

// Other stuff

struct
{
uint16_t ADC1;
uint16_t ADC2;
uint16_t ADC3;
uint16_t ADC4;
uint16_t Acc_X;
uint16_t Acc_Y;
uint16_t Temp1; // DS18s20
uint16_t Temp2;
uint16_t Voltage;
} MyIOs;

GpsInfo_t MyGPS;
void CPU_init(void);

int main(void)
{
CPU_init();

OS_CreateTask(TaskSD,TID_SD);
OS_CreateTask(TaskDS1820,TID_DS);
OS_CreateTask(TaskADC,TID_ADC);
OS_CreateTask(TaskLCD,TID_LCD);
OS_CreateTask(TaskNMEA,TID_NMEA);

OS_CreateAlarm(ALM_ADC, TID_ADC);
OS_CreateAlarm(ALM_LCD, TID_LCD);
OS_CreateAlarm(ALM_Timeout, TID_NMEA);

OS_StartExecution();
while(1)
{
// take care of the RTC
}
}

void TaskSD(void)
{
while(1)
{
OS_WaitEvent(EVNT_Go); // sent by ADC

OS_MutexGet(MutexGPS);
// do write actual coordinates
OS_MutexRelease(MutexGPS);

OS_MutexGet(MutexIO);
// do write the stuff
OS_MutexRelease(MutexIO);
}
}

void TaskDS1820(void)
{
while(1)
{
OS_WaitEvent(EVNT_Go); // sent by LCD, 1s beat
// do DS18s20 acquisition

//use
OS_WaitTicks(75); //750ms conversion time

OS_MutexGet(MutexIO);
// set values
OS_MutexRelease(MutexIO);
}
}

void TaskADC(void)
{
OS_SetAlarm(ALM_ADC,10); // every 100ms
while(1)
{
OS_WaitAlarm(ALM_ADC);
OS_SetAlarm(ALM_ADC,10); // every 100ms

OS_MutexGet(MutexIO);
// set values
OS_MutexRelease(MutexIO);
if(/*big value change and voltage ok*/1)
{
OS_SetEvent(TID_SD,EVNT_Go);
}
}
}

void TaskLCD(void)
{
OS_SetAlarm(ALM_LCD,100); // every second
while(1)
{
OS_WaitAlarm(ALM_LCD);
OS_SetAlarm(ALM_LCD,100); // every second

OS_MutexGet(MutexIO);
// display stuff
OS_MutexRelease(MutexIO);

OS_MutexGet(MutexGPS);
// display actual coordinates
OS_MutexRelease(MutexGPS);

OS_SetEvent(TID_DS,EVNT_Go); // wake up the DS18s20 Task
}
}

void TaskNMEA(void)
{
uint8_t byte,ret,i;
uint8_t packet[50];

while(1)
{
ret = OS_WaitEventTimeout(EVNT_Go|EVNT_Error, ALM_Timeout, 200);
// sent by ISR, new message complete, if no Message, timeout.after 2 s
if(ret == 0 || ret & EVNT_Error)
{
while(!OS_QueueOut(&NMEAQueue, &byte)); // empty the queue

// invalidate GPS data
}
else
{
//operate queue
for(i=0;i<sizeof(packet);i++)
{
if(!OS_QueueOut(&NMEAQueue, &byte))
{
packet[i] = byte;
}
else
{
break;
}
}
//process message byte...
OS_MutexGet(MutexGPS);

// add actual coordinates
nmeaProcessPacket((char*)packet,&MyGPS);

OS_MutexRelease(MutexGPS);
}
}
}

void CPU_init(void)
{
// init cyclic ISR
TCCR1A = 0b00000000;
TCCR1B = 0b00000010; //1250 kHZ timer ck
OCR1A = 12500; //interrupt every 10ms at 10MHz
TIMSK1 |= 1<<OCIE1A;
}

#if OS_USEEXTCHECKS == 1
void OS_ErrorHook(uint8_t ErrNo)
{
// you custom error handling
}
#endif