FabOS

Programmers guide

# API reference

## Defines in FabOS.h
#define NUMMBOX 5
sets the number of mailboxes
never >8

#define NUMTASKS 3
Sets the numer of tasks excluding the idle task. (number of CreateTask - calls)
never >8

#define UNUSEDMASK 0xee
Sets the value to be written into unsed memory.
Used by "OS_get_unused_Stack()"

#define OS_ScheduleISR TIMER1_COMPA_vect
Sets the interrupt vector used for scheduling.
The user has to set up the cyclic timer interrupt.
If any additional code has to be executed in this interrupt, the Function "OS_CustomISRCode() " can be filled with this code.

## void OS_TaskCreate( uint8_t taskNum, void (*t)(), uint8_t *stack)
Creates a task. This function is realized as a macro to simplify the API;
First Parameter is the task number, where also the number defines priority. Task 0 has the highest priority. Task 7 is the lowest priority. The maximum bumber of tasks is 8. (so the highest number here is 7)
Second parameter is a pointer to a void function, which implements the task. Inside this function all OS – API calls can be used.
Third parameter is a pointer to the stack array of this task. Each task needs its own stack space. The remaining stack size can be checked by the OS_get_unused_stack() function.
## void OS_TaskDestroy( int8_t taskNum ); // destroy task
Destroys a task, but does not free any memory.
## void OS_StartExecution()
Start the Operating system; This function returns, if no task is to be run. The code after this function call is the idle task. So this function must be followed by an infinite loop.
## void OS_mutexGet(int8_t mutexNum)
Get a Mutex when entering a critical section. If the mutex is occupied, the scheduling will switch to the task, which is blocking the mutex.
One OS-tick will be lost in this implementation.
The number of mutexes limited to 8.

## void OS_mutexRelease(int8_t mutexNum);
Release the Mutex at the end of a critical section.

## void OS_Wait( uint16_t ) ;
OS API: Wait for a certain number of OS ticks
## void OS_SetAlarm(uint8_t TaskID, uint16_t numTicks );
set Alarm and continue
## void OS_WaitAlarm(void);
set Alarm and continue
## void OS_CustomISRCode() ;

## uint16_t OS_get_unused_Stack (uint8_t*)

## ISR (OS_ScheduleISR)__attribute__ ((naked,signal));
Internal, not to be called by the application;
OS tick interrupt function (vector defined above)
## void OS_TaskCreateInt( uint8_t taskNum, void (*t)(), uint8_t *stack, uint8_t stackSize )
Internal, not to be called by the application;
Create the task internal
## int8_t OS_GetNextTaskNumber()
internal: determine the next task to be run according priority.
## void OS_Reschedule(void)__attribute__ ((naked))
Trigger re-scheduling according the task priorities.
Mostly used internal.
(__attribute__ ((naked)) )
## void OS_mBoxPost(int8_t,int16_t)

## int16_t OS_mBoxPend(int8_t) ;

OS buffers

#define BUFFER_SIZE 64 // must be 2^n (8, 16, 32, 64 ...)
#define BUFFER_MASK (BUFFER_SIZE-1) // don't forget the braces

struct Buffer

uint8_t BufferIn(uint8_t byte)

uint8_t BufferOut(uint8_t *pByte)